## Slide 1
A Non-homogeneous Time Mixed Integer LP Formulation for Traffic Signal Control
Iain Guilliard, Scott Sanner, Felipe Trevizan, Brian Williams
Notes: 1. Title Slide: I'm going to talk about recent progress in how to globally optimize traffic signals using MILPS.

## Slide 2: Motivation
Notes: Fixed plan:
- not adaptive to changes in traffic
- fixed objective: worst case or average, etc
Adaptive:
- old - from 1960's
- reactive rather than predictive

## Slide 3: Control methods
Suboptimal
  Fixed Time Control
  Adaptive Control: e.g. SCOOT and SCATS
  Good: scalable
  Bad: no performance guarantee
Locally optimal:
  e.g. SURTRAC
  Good: decentralized control
  Bad: myopic
Globally optimal
  e.g. CTM, LTM
  Good: best solution possible
  Bad: scalability
Notes: Fixed-time: in practice, different plans for different times of day + actuation.
Optimal controllers: typically two parts: traffic model + optimization algorithm
Cost: EXPONENTIAL FUNCTION number of intersections by number of time samples

## Slide 4: In this work
We present the Queue Transmission Model that:
Is globally optimal
  We take advantage of the new developments in MILP solvers
Allows arbitrary topology
  Grids and asymmetric intersections
Scales to many intersections
  3 continuous variables, 1 binary per link
  We use non-homogenous time steps to decrease the size of the problem

## Slide 5: Homogeneous vs Non-Homogeneous
Time discretization:
  Homogenous: uniform
  Non-homogenous: arbitrary
Advantages of non-homogeneous:
  Increase spatial horizon
  Offers fidelity trade off
Non-Homogeneous
Homogeneous
Homogeneous
Non-Homogeneous
Notes: Time Dilation

## Slide 6: QTM Example

## Slide 7: QTM Example – Flow with fixed control

## Slide 8: QTM Example – Queuing Behavior

## Slide 9: QTM Example – Platoons

## Slide 10: QTM Example – Turn Probabilities

## Slide 11: QTM – Variables and Parameters

## Slide 12: QTM – Variables and Parameters
F
I
F
O

## Slide 13: QTM – Variables and Parameters
FIFO
Notes: Think of vertically stacked queue as horizontal that spills back up the approach

## Slide 14: QTM – Variables and Parameters
free flow
congested
separating shockwave
Notes: Folded together
Capture two regimes: free flow and congested with separating shock

## Slide 15: QTM - Dynamics
c3
c2
c1
CTM
3 cells
c3
c2
c1
QTM
CTM
9 cells
c4
c5
c6
c7
c8
c9
Link
traffic state
platoon
queue at light
vf
free flow
congested
Notes: CTM based directly on wave equations
CTM fixed cell boundaries
CTM Mismatch cell boundaries mismatch with link boundaries

## Slide 16: QTM – Non-homogeneous time steps

## Slide 17: QTM – Non-homogeneous time steps

## Slide 18: QTM – Non-homogeneous time steps

## Slide 19: QTM – Non-homogeneous time steps

## Slide 20: Discretization – Convergence
Homogeneous
Non-homogeneous

## Slide 21: Integration V(x,y)
Notes: Need to find volume of traffic that was travelled down link and arrived at the stopline during current interval
Integration components identified in a pre computation step

## Slide 22: Integration V(x,y)

## Slide 23: Integration V(x,y)

## Slide 24: Integration V(x,y)

## Slide 25: Update Step
Traffic arriving at stop line during interval n

## Slide 26: Phase & Cycle Duration Control
Ramp
Hold
Reset
Cycle time

## Slide 27: Objective Function
In flow
Out flow
Delay
Travel Time

## Slide 28: Objective Function
In flow
Out flow
Delay
Travel Time

## Slide 29: Objective Function
In flow
Out flow
Delay
Travel Time

## Slide 30: QTM Example: with optimized control

## Slide 31: Example: Delay Map, fixed vs optimized
Fixed
QTM Optimized

## Slide 32: Experiments - Networks
Input Demand Profile

## Slide 33: Experiments – Receding Horizon Control
Non-Homogeneous steps
Homogeneous steps

## Slide 34: Experiments – Receding Horizon Control
Non-Homogeneous steps
Homogeneous steps
Executed control plan

## Slide 35: Experiments – Receding Horizon Control
Non-Homogeneous steps
Homogeneous steps
Demand profile

## Slide 36: Experiments – Optimal Reference
Directly solve single homogenous discretization as an optimal reference solution
single homogenous discretization

## Slide 37: Results - Convergence
Increasing travel time
Time samples / planning horizon
Homogeneous
Non-
Homogeneous
Non-
Homogeneous
Ref

## Slide 38: Results - Quality
F
Increasing travel time
Time samples / planning horizon
Ref

## Slide 39: Extensions
Globally Optimal Fixed Time Control
  Simulate fixed adaptive controllers (e.g. SCATS)
  Pre-compute optimal schedules for fixed controllers
Light Rail Schedules
  nullify the impact of introducing light rail
Uncontrolled intersections
  Optimize via neighboring intersection signals

## Slide 40: Globally Optimal Fixed Time Control

## Slide 41: Fixed Time Control – micro-simulation
Distance
Time
Demand Profile

## Slide 42: Light Rail – Network 1

## Slide 43: Light Rail – Fixed vs Optimized
Fixed – side street
Fixed – arterial
Optimized – side street
Optimized – arterial

## Slide 44: Light Rail – Network 2

## Slide 45: Light Rail – Delay Heat Map 3400 vph
Optimized
Fixed

## Slide 46: Light Rail – Delay Heat Map 4300 vph
Optimized
Fixed

## Slide 47: Uncontrolled Intersections

## Slide 48: Conclusion
Presented Queue Transmission Model (QTM)
  Globally optimal
  Allows arbitrary topology
  Scales to many intersections
Main insight: non-homogenous time discretization
Compared to homogeneous solution:
  Faster convergence
  Same or better solution quality
Extensions:
  Globally optimal fixed time control
  Mitigation of light rail impact
  Coordination of uncontrolled intersections
Notes: Compare optimized plans with SCATS/SCOOT to see if there is a better heuristic

## Slide 49: Future Work
Solve iteratively
Close the loop
  Learn QTM parameters from data
Compare QTM:
  with CTM and LTM MILPS
  with SCATS simulator
Scale bigger
  Use bigger nodes on AWS
Code on Github:
  github.com/iainguilliard/QTM_Traffic_Model
Notes: Compare optimized plans with SCATS/SCOOT to see if there is a better heuristic

## Slide 50
Thank you!
Questions?

## Slide 54: Extras

## Slide 55: Example: Fixed Control with QTM flow

## Slide 56: Example: QTM optimized control

## Slide 57: Globally Optimal Fixed Time Control

## Slide 58: Fixed Time Control - Compared